## Slide 1
References: R.S. Wilcox et al., Nuclear Fusion (submitted)
This work was supported in part by the US Department of Energy under DE-FC02-04ER54698, DE-AC05-00OR22725, DE-AC52-07NA27344, DE-NA0003525, and DE-SC0023378.
Correlating Pedestal Density Structure with Divertor Target Temperature in DIII-D
E.J.B. Dreisbach, R.S. Wilcox, J.M. Canik, F. Conti, R. Hood, A.G. McLean, A.L. Moser, T.H. Osborne, M.W. Shafer, C.K. Tsui, H.Q. Wang, T.M. Wilks
Divertor target diagnostics disagree @ low temperatures
ELM Filtering plays a minor role in data processing
Determination of the Te,sep plays a significant role in the pedestal density ratio
A single, unified function does not appear to be representative of all data, or even a subset of data where individual variables are held fixed, that could be used to extrapolate a causal relationship in a predictive simulation framework.
Power balance refinement: improved methodology for picking correct Te,sep values
Broaden the datasets used (shots/experiments) and separate regimes (attached vs near-detached)
Account for plasma shape and impurity seeding
Limit data to only include probes within 1-2 heat flux from the divertor
MOTIVATION & FRAMEWORK
METHODOLOGY
LSN TS data
  Key Questions:
  - Does this hold across other experiments?
  - Under what conditions does it change or break down?
Background
Experimental setup and divertor configurations
Correlating pedestal density profiles with divertor electron Temperature may inform edge transport modeling & conditions for reaching detachment
  Experiment 1 – Canik Database
  Towards a self-consistent EPED-SOLPS Coupled Integrated Model
  Experiment 2 – Moser Database
  Divertor closure impact on detachment and pedestal shape
  Experiment 3 – Wang Database
  Divertor detachment and pedestal structure in a closed Upper divertor
upper
ELM filtering
  Core Plasma Density shows pedestal buildup, impacted by ELM crashes
  Heat Flux sharp, periodic spikes correspond to ELM events
  Stored Energy recovers between ELMs, drops during each crash
  Peaks included by threshold identifies ELM crashes
Evolution of median temp measurements over ELM cycles informs % of data to accept
Optimal fractional period only accepts steady-state data
  Consistent range of 10-99% used for this analysis
Exclude evolving temp trends → correspond to ELM come-down/build-up
Data averaging methods
LP data
  Median time average
  Weighted spatial average:
TS data
  Weighted time average
  No spatial averaging necessary
Langmuir Probe ELM filtered Profiles
Shifting the separatrix position in density profiles
Adjusted the flux coordinate mapping to align with upstream TS measurements
Select ne,sep based on the electron temperature at the separatrix (Te,sep)
Sweeping from 60-140 eV in Te,sep shifted the density ratio by a factor of ~2-3, depending on the divertor configuration
Diagnostics for determining target electron Temperature
Consistent IP and power across different divertors
Power variation using consistent current (IP) and divertor configuration
  ELM Peak 
IP variation using consistent power and divertor configuration
LP data overestimates Te,targ at low temperatures (<5-10 eV)
  Curve fit → Saturating Offset Exponential
Shots @ various input powers (~3-9 MW) fall along similar curves
Some datasets show consistent curves between variables, others diverge significantly
  Divertor geometry and plasma shape affect correlation curve
  Upper divertor shows steepest ratio rise @ low Te,targ
ne,ped/ne,sep increases with current during attachment
Future data processing refinements
  Level differs by geometry
    Closed divertors  ratio >15 eV reaches ~2.5-3.5 range
    Open divertors  ratio >15 eV reaches ~1.8-2.2 with a broader scatter
CORRELATION ANALYSIS & RESULTS
Edge-core coupling: pedestal structure and divertor electron Temperature
  Thomson Scattering (TS) Data, Bottom Channel
  Langmuir Probe (LP) Data, Outer Strike Point
Conclusion
Acknowledgments & References
Tamás Szabolics, EUROfusion
Project Goal: Investigate if there exists an empirical correlation between pedestal structure and particle Temperature at the divertor
Pedestal: narrow transport barrier that sets boundary conditions which influence core performance
ne,ped  upstream density profile
Separatrix: boundary surface separating the core from the edge plasma & guides field lines to the divertor
ne,sep  downstream density profile
Divertor: location on the reactor wall where all the heat and particle flux is ‘dumped’
Goal of detachment → plasma cools sufficiently before reaching the wall
Te,targ  electron Temperature at the target (divertor)
Sensitivity scans show density ratio dependence on Te,sep